Onity offline lock battery maintenance

** Door can be opened with XPP Programmer **

When door batteries are low or dead, use the following method to open the door.

- load locking plan for respective door

- login to XPP Programmer

- choose XPP option of “Power the Lock” or “Open Lock”

Steps to replace batteries:

- Download activity data, if possible, prior to performing maintenance with XPP programmer.

- Access the battery compartment. 

- door handle version   
- remove Torx security screw 
	(ADM, LCSEE, MAE have tool)
	on handle and below handle
- remove handle
- left cover up and tilt out from the top
- batteries are at the top
- make sure wires are not pinched when replacing cover

 
- panic bar version A  
- remove Phillips screws from end of 	panic bar
- slide cover to left to expose 	batteries
- when closing up, make sure clip on 	slide cover is over the guide rails
- make sure wires are not pinched when closing cover

- panic bar version B 
- remove Phillips screws from edge of door to expose batteries
- make sure wires are not pinched when closing cover

- Replace as needed (high use = 6 months, other = 12 months) with Energizer Industrial type.

- Must update lock to restart clock even though programming is retained.

- Test door operation.