| Integra Lock Light Indications |
| --- |
| Lights | Description | What It Means | What To Do |
|  | Steady Green | Unlocked | * Enter Room |
|  | Immediate Red | The card isn’t authorized for that door or wrong room. The user is not assigned to the doors locking plan. The Card has Expired. The Card was voided. | * Read the card, verify the encoded NAME/template, encode a new card if necessary. * Read the card, verify expiration date and assignment to locking plan of the door. * Encode a New Card. |
|  | Alternating Flashing Green And Flashing Red | The deadbolt is thrown. Improper Lock installation. The wire was pinched and shorted. | * Retract the deadbolt, or use PP to open the door. * Remove and reinstall the lock with the deadbolt fully retracted. * Remove the lock & check for a shorted wire or incorrect micro-switch setting. |
|  | Delayed Red | Card is blank, or damaged. The card was inserted incorrectly. The card was left in the lock for too long. The Internal card read head requires service or cleaning | *Read the card; if data is missing, encode a new card. * Properly re-insert/remove the card into the lock. * Remove card, wait, then re-insert and remove it more quickly. * Test the lock with the portable programmer; replace lock if necessary. |
|  | Flashing green | Unlocked; door is in "Office Mode". | * Enter the room OR to remove office mode. * Double-dip a card with owner function on it, a red light will flash once, lock will return to normally locked mode. |
|  | Flashing Red | The Lock was blocked with a blocking Card. | * Use a card with OWNER enabled to bypass the block OR to remove the block. * Insert a blocking card to unblock the lock (RED light will flash once indicating removal of block) |
|  | Steady Red and Green after Insert and Removal of Card | The Lock is in "Security Mode", Valid card and pin# required for entry access | *Insert and remove your card, enter your personal 4-digit pin# to gain access. |
|  | Steady Green with Flashing Red | The batteries are in the lock are low. | * Replace the Batteries and update the lock. |