Onity XPP programmer battery maintenance

Note The XPP programmer can be on 24/7 charging because an internal regulator only charges batteries as needed.

Steps to replace batteries:

- Download data from XPP programmer, if possible, prior to performing maintenance.

- Remove power charger connection.

- Remove back cover on XPP programmer to access battery compartment.

- Replace rechargeable batteries as needed with Energizer Rechargeable type.  These should be nickel-metal hydride (NiMH) cells only.

- Recharge unit for 8-12 hours.

- Test XPP programmer operation.