Extended Portable Programmer:

The extended portable programmer (XPP) is a portable device to update locks and read lock openings, in other words, it allows you to transfer changes that are made to the Integra database to the lock or locks.  Without a XPP, managing your locks would be impossible.

The XPP is a Powerful Device, in the wrong hands it could be used to modify or gain access to your locks.

Your XPP should be kept in very secure place when not being used!

## Connecting the Extended Portable Programmer to the PC:

To connect a XPP to the PC, you need to use a serial cable similar to the one shown in the figure.

Each end of the Serial Cable looks similar to the image in following figure.

Connect one end of the Serial Cable to your computer’s serial port.  Your computer’s serial port is usually located on the back of your computer.  Make sure you connect the cable to COM 2, some computers have multiple serial ports – COM 2 usually has number ‘2’ near it to indicate that it is COM 2.

Connect the other end of the serial cable to the top of the XPP which has the exact same type of serial connector as the PC.

## Replacing the Batteries:

On the Back of the XPP is a plate which you can remove to access the battery compartment. The Programmer takes 4 AA batteries.

## Updating a Lock:

- Turn the XPP to on by pressing the ON button; you should get a soft beep telling you that the programmer is on as well as information displayed on the LCD screen.

- Next from the Main Menu click on Communication then XPP, you should get a screen similar to the following.

- Click on the  button. If Integra can communicate with the programmer then you will see the following window.

- Select the  option by clicking the radio button next the item - you should then get a screen like the one shown on the next page.

- Select the door(s) you want to update by double clicking on the door from the list on the left. The door should then appear on the list on the right.  If you accidentally select a door that you don’t want to update, just double click on it from the right to remove it. When you are finished selecting the doors you want to update click the ‘Close’ button.

You should now be back at XPP Screen.

- Select the operators to load into the programmer by placing a checkmark beside their names.

- Click on the    button to load the data for each lock that needs updated onto the XPP, you should get a progress bar and then a beep with a message saying:

- Click OK.

- Click the Close Button – the XPP should shut off on its own.

- Disconnect the XPP from the serial cable and go the lock that need updated.

- Connect round plug end of the XPP into the hole under the front of     the lock, as shown in following figures.

- Press the ON Button to turn the XPP On.

- Use the UP and DOWN ARROWS to highlight UPDATE LOCK then press ENTER.

- Use the UP, DOWN, and N UP buttons to scroll through all the Not Updated doors. Highlight the door you want to Update and press ENTER. The XPP should make beeping noises as it updates the lock and should display the name of the lock being updated.

- After the XPP is done updating it should give you a message of “OK, Ready Press any key to Exit”.

- Press the OFF Button and disconnect the XPP from the lock.

- Repeat steps 9 through 13 for each lock you need to update.

The lock or locks should now be updated with your changes – Users that aren’t supposed to have access should no longer be able to get into the room.

Once a lock has been updated, the Software will need to know that the door has been updated. Once you have updated all the locks that needed updated, bring the XPP back and connect it up to the PC.

- Follow steps 1 through 3 previously outlined to connect the XPP to the Integra system. You should see the following screen.

- Click on ‘Yes’ to read openings from the XPP. The following screen will appear when Integra is finished reading the openings from the XPP.

- Click on ‘Ok’ then on ‘Close’.